## Slide 1: Capstone Project A Scalable and Parallelizable Multi-Agent Reinforcement Learning Framework for Cooperative and Competitive Autonomous Vehicles
Chinmay Samak
PhD Candidate, CU-ICAR
csamak@clemson.edu
Tanmay Samak
PhD Candidate, CU-ICAR
tsamak@clemson.edu
AuE-8930 Computing and Simulation for Autonomy

## Slide 2: Project Management
Scalable and Parallelizable Multi-Agent Reinforcement Learning for AVs

## Slide 3
Set up high-fidelity 3D simulation platform based on real-world vehicle/environment representations (real2sim transfer) [Tanmay]
Set up modular and scalable simulation framework using object oriented programming (OOP) [Chinmay]
Set up intelligent agent/environment parallelization framework for accelerating RL training [Tanmay]
Formulate multi-agent reinforcement learning (MARL) problems for: [Tanmay]
  Cooperative MARL - collaborative intersection traversal
  Competitive MARL - head-to-head autonomous racing
Implement the formulated deep reinforcement learning (DRL) pipeline and conduct parallelized training [Chinmay]
Deploy and analyze the trained policies and procedures to comment on the aspects of “computing and simulation for autonomy” [Chinmay]
Planned Project Objectives
Note: The name in square bracket indicates primary responsibility and NOT necessarily contribution. Both members worked together and contributed equally to this project.

## Slide 4
AuE-8930 Capstone Project (Fall 2023) |  |  |  |  |  |  |  | 
Task | 10/17 | 10/24 | 10/31 | 11/07 | 11/14 | 11/21 | 11/28 | 12/05
Announcements |  |  |  |  |  |  |  | 
Project Proposal |  |  |  |  |  |  |  | 
Phase 1 |  |  |  |  |  |  |  | 
Phase 2 |  |  |  |  |  |  |  | 
Phase 3 |  |  |  |  |  |  |  | 
Project Presentation |  |  |  |  |  |  |  | 
Project Report |  |  |  |  |  |  |  | 
Planned Project Timeline

## Slide 5: Research Motivation
Scalable and Parallelizable Multi-Agent Reinforcement Learning for AVs

## Slide 6
Reinforcement learning
  Learning through experience
Multi-agent reinforcement learning
  Complex and dynamic interactions
  Cooperative and competitive scenarios
Autonomous vehicles
  Cooperation: autonomous driving
  Competition: autonomous racing
  Coopetition: cooperation and competition
Multi-Agent Reinforcement Learning

## Slide 7
Existing approaches
  Multiple simulation instances
  Multiple robots in single simulation instance
Challenges
  Unnecessary computational overhead
  Exteroceptive perception modalities
Ideal approaches
  Parallelize only what is required
  Environment parallelization
  Agent parallelization
Simulation Parallelization

## Slide 8: Literature Survey
Scalable and Parallelizable Multi-Agent Reinforcement Learning for AVs

## Slide 9
T. Samak, C. Samak, S. Kandhasamy, V. Krovi, and M. Xie, “AutoDRIVE: A Comprehensive, Flexible and Integrated Digital Twin Ecosystem for Autonomous Driving Research & Education,” Robotics, vol. 12, no. 3, p. 77, May 2023, doi: https://doi.org/10.3390/robotics12030077
Comparative Analysis of Hardware Platforms

## Slide 10
W. Ding, C. Xu, M. Arief, H. Lin, B. Li and D. Zhao, “A Survey on Safety-Critical Driving Scenario Generation—A Methodological Perspective,” in IEEE Transactions on Intelligent Transportation Systems, vol. 24, no. 7, pp. 6971-6988, July 2023, doi: 10.1109/TITS.2023.3259322
Comparative Analysis of Simulation Platforms

## Slide 11
Vehicle | Mobile Base | Battery | Computer(s) | Sensor(s) | Actuator(s) | Developer | Release | Cost
Nigel | Open-Source | 5200 mAh | Jetson Nano or Jetson Orin Nano | RPLIDAR A-1, Pi-Cameras, Intel RealSense D435i, 9-Axis IMU, 6-Axis IPS, Encoders, Microphone, Steering Feedback, Throttle Feedback | DC Motors, Steering Servo(s) | CU-ICAR + NTU + SRMIST | 2021 | $450
Source: https://autodrive-ecosystem.github.io
=
AutoDRIVE Ecosystem
Simulation Quality | Physics Engine | Graphics Rendering | Vehicle Dynamics Support | Sensor Support | API Support | Developer | Cost | Open Source | Applications
3D | PhysX | Unity HDRP | Full car model for lateral, longitudinal, vertical and RPY dynamics with tire-terrain interaction | 2D/3D LIDAR, Camera, GNSS, IPS, IMU, Encoders Steering Feedback, Throttle Feedback, State Variables | ROS, ROS 2, Python, C++, MATLAB, Simulink, Webapp | CU-ICAR, NTU, SRMIST | Free | Yes | Exploration, education and research
Develop autonomy algorithms using flexible APIs
Simulate for initial prototyping and corner-case analysis
Deploy on mechatronic testbed for real-world validation
Small, mid and full-scale vehicles and infrastructure
Autonomous driving + smart-city applications
Affordable cost and completely open-source
Resources:
  Website
  Paper
  GitHub
  YouTube

## Slide 12
Article/Author | Methodology | Tools/Frameworks | Observations | Actions | Application | Summary | Year
Semnani et al. [3] | FMP+DRL | Python Simulation |  | for differential drive robots (2D/3D) | Motion planning | Hybrid algorithm of deep reinforcement learning (RL) and force-based motion planning (FMP) to solve distributed motion planning problem in dense and dynamic environments. | 2020
Long et al. [4] | DRL | Stage Simulator |  | for differential drive robots | Collision avoidance | End-to-end decentralized sensor-level collision avoidance policy for multi-robot systems. | 2018
Aradi et al. [5] | DRL | N/A | N/A | N/A | Motion planning | Survey on hierarchical motion planning using DRL. | 2020
Wang et al. [6] | DRL | Custom |  | for differential drive robots | Motion planning | End-to-end method to train directly from each robot-centered, relative perspective generated image, and each robot’s reward as the input. | 2020
Zhou et al. [7] | DRL | Python Simulation |  | for USVs | Formation and collision avoidance | DRL for USV formation path planning with specific focus on a reliable obstacle avoidance in constrained maritime environments. | 2020
Sivanathan et al. [8] | DRL | MARL Simulator |  | for differential drive robots | Motion planning | Decentralized motion planning framework for addressing the task of multi-robot navigation using deep reinforcement learning. | 2020
Article/Author | Methodology | Tools/Frameworks | Observations | Actions | Application | Summary | Year
Semnani et al. [3] | FMP+DRL | Python Simulation |  |  | Motion planning | Hybrid algorithm of deep reinforcement learning (RL) and force-based motion planning (FMP) to solve distributed motion planning problem in dense and dynamic environments. | 2020
Long et al. [4] | DRL | Stage Simulator |  |  | Collision avoidance | End-to-end decentralized sensor-level collision avoidance policy for multi-robot systems. | 2018
Aradi et al. [5] | DRL | N/A | N/A | N/A | Motion planning | Survey on hierarchical motion planning using DRL. | 2020
Wang et al. [6] | DRL | Custom |  |  | Motion planning | End-to-end method to train directly from each robot-centered, relative perspective generated image, and each robot’s reward as the input. | 2020
Zhou et al. [7] | DRL | Python Simulation |  |  | Formation and collision avoidance | DRL for USV formation path planning with specific focus on a reliable obstacle avoidance in constrained maritime environments. | 2020
Sivanathan et al. [8] | DRL | MARL Simulator |  |  | Motion planning | Decentralized motion planning framework for addressing the task of multi-robot navigation using deep reinforcement learning. | 2020
DRL-FMP hybrid control framework [3]
Collision avoidance using DRL [4]
Decentralized motion planning using DRL [8]
State-of-the-Art: Cooperative DRL

## Slide 13
Article/Author | Methodology | Tools/Frameworks | Observations | Actions | Application | Summary | Year
Fuchs et al. [9] | DRL | Gran Turismo Sport |  | for full-scale Ackermann steered vehicle | Autonomous racing | Learning-based system for autonomous car racing by leveraging a course-progress proxy reward and deep reinforcement learning. | 2020
Song et al. [10] | DRL | Gran Turismo Sport |  | for full-scale Ackermann steered vehicle | Autonomous overtaking | Curriculum-learning-based method to tackle the autonomous overtaking problem using DRL. | 2021
Samak et al. [11] | Hybrid IL+RL | AutoRACE Simulator |  | for full-scale Ackermann steered vehicle | Autonomous racing | Hybrid imitation-reinforcement learning architecture to train a rigorous end-to-end control strategy for autonomous vehicles aimed at minimizing lap times in a time attack racing event. | 2020
Betz et al. [12] | Mixed | N/A | N/A | N/A | Autonomous racing | Survey on autonomous vehicle racing. | 2022
Article/Author | Methodology | Tools/Frameworks | Observations | Actions | Application | Summary | Year
Fuchs et al. [9] | DRL | Gran Turismo Sport |  |  | Autonomous racing | Learning-based system for autonomous car racing by leveraging a course-progress proxy reward and deep reinforcement learning. | 2020
Song et al. [10] | DRL | Gran Turismo Sport |  |  | Autonomous overtaking | Curriculum-learning-based method to tackle the autonomous overtaking problem using DRL. | 2021
Samak et al. [11] | Hybrid IL+RL | AutoRACE Simulator |  |  | Autonomous racing | Hybrid imitation-reinforcement learning architecture to train a rigorous end-to-end control strategy for autonomous vehicles aimed at minimizing lap times in a time attack racing event. | 2020
Betz et al. [12] | Mixed | N/A | N/A | N/A | Autonomous racing | Survey on autonomous vehicle racing. | 2022
DRL-FMP hybrid control framework [9]
Autonomous overtaking using DRL [10]
Hybrid IL+RL architecture for autonomous racing [11]
State-of-the-Art: Competitive DRL

## Slide 14: Digital Twin Creation
Physically and Graphically Accurate Digital Twins for Sim2Real-Worthy RL Training

## Slide 15: Digital Twin Capabilities of AutoDRIVE Ecosystem
Source: AutoDRIVE Ecosystem
Husky (On/Off-Road Skid-Steer Robot)
Hunter SE (On/Off-Road Ackermann Steered Vehicle)
Nigel (Native Vehicle)
F1TENTH (1/10th Scale Racecar)
RZR (Recreational Off-Highway Vehicle)
OpenCAV (On-Road Commercial Vehicle)
SMALL-SCALE
MID-SCALE
FULL-SCALE

## Slide 16
Nigel
  1:14 scale
  Autonomous driving
F1TENTH
  1:10 scale
  Autonomous racing
Digital twinning
  Dynamics interface
  Perception interface
Digital Twins of Nigel and F1TENTH

## Slide 17
Rigid-body dynamics
Suspension dynamics
Tire dynamics
Actuator dynamics
Digital Twins: Dynamics Interface

## Slide 18
Throttle sensor
Steering sensor
Indoor positioning system
Inertial measurement unit
Incremental encoders
LIDAR
Cameras
Digital Twins: Perception Interface

## Slide 19: Cooperative Multi-Agent RL
Collaborative Intersection Traversal

## Slide 20
POMDP
  Limited state-sharing (V2V)
Observation space
  Relative goal position
  Relative peer poses
  Absolute peer velocities
Action space
  Discrete throttle
  Discrete steering
Reward formulation
  Goal
  Collision
  Lanes
Problem Formulation

## Slide 21
Training hardware
  CPU: 12th Gen Intel Core i9-12900H 2.50 GHz
  RAM: 32.0 GB (31.7 GB usable)
  GPU: NVIDIA GeForce RTX 3080 Ti
Non-parallelized training time
  3.543 hours
Scenarios
  Single-agent learning
  Multi-agent learning
Training analysis
  Cumulative reward
  Episode length
  Policy entropy
MARL Training
Cumulative Reward
Training Steps
Training Steps
Training Steps
Training Steps
Training Steps
Training Steps
Episode Length
Policy Entropy
Policy Entropy
Episode Length
Cumulative Reward
Single-Agent Scenario
Multi-Agent Scenario

## Slide 22
MARL Deployment
Single-Agent Learning Scenario
Multi-Agent Learning Scenario

## Slide 23: Competitive Multi-Agent RL
Head-to-Head Autonomous Racing

## Slide 24
POMDP
  No state-sharing
Observation space
  Own velocity
  Sparse LIDAR measurements
Action space
  Discrete throttle
  Discrete steering
Reward formulation
  Collision
  Checkpoints (19 virtual ckpts)
  Lap completion (1 virtual ckpt)
  Best time
  Velocity
Problem Formulation

## Slide 25
Training hardware
  CPU: 12th Gen Intel Core i9-12900H 2.50 GHz
  RAM: 32.0 GB (31.7 GB usable)
  GPU: NVIDIA GeForce RTX 3080 Ti
Non-parallelized training time
  4.211 hours (SOTA: >72 hours with better compute [9])
Training analysis
  BC Loss
  GAIL reward
  Curiosity reward
  Extrinsic reward
  Episode length
  Policy entropy
MARL Training
Behavioral Cloning Loss
Training Steps
Training Steps
Training Steps
Training Steps
Training Steps
Training Steps
Curiosity Reward
Episode Length
Policy Entropy
Extrinsic Reward
GAIL Reward

## Slide 26
MARL Deployment
Block-Block-Overtake
Let-Pass-and-Overtake

## Slide 27: Scalable Simulation Parallelization
Scalable and Parallelizable Multi-Agent Reinforcement Learning for AVs

## Slide 28
Scalable parallelization architecture
  Object oriented programming (OOP)
  CPU multi-threading
  GPU instancing
  Isolation in different “layers” of simulation
  Environment on “default” layer
  Each family of multi-agent system on same layer
Parallel perception, collision and interaction
  Interoceptive sensors have little to no issue in parallelizing
  Camera: rendering culling mask only for specific layers
  LIDAR: raycasting returns hit only for specific layers
  Interactions and collision-checks between specific layers
Simulation Parallelization
-Environments
-Agents
Note: The term “family” here denotes the problem formulation for multi-agent RL. In our case, this translates to 4 agents for the intersection traversal scenario and 2 agents for the autonomous racing scenario.

## Slide 29
Cooperative MARL parallelization
  {1, 5, 10, 15, 20, 25} environments
  {1x4, 5x4, 10x4, 15x4, 20x4, 25x4} agents
Competitive MARL parallelization
  1 environment
  {1x2, 2x2, 4x2, 6x2, 8x2, 10x2} agents
Computational analysis
  Training time (hours)
  Reduction in training time (%)
Parallel MARL
Chart: Training Time
| 1 | 5 | 10 | 15 | 20 | 25
Series 1 | 3.543 | 1.28 | 0.963 | 0.915 | 0.866 | 0.84
Chart: Reduction in Training Time
| 1 | 5 | 10 | 15 | 20 | 25
Series 1 | 0 | 63.872 | 72.82 | 74.174 | 75.557 | 76.291
Chart: Training Time
| 1 | 2 | 4 | 6 | 8 | 10
Series 1 | 4.211 | 3.095 | 2.528 | 2.336 | 2.249 | 2.148
Chart: Reduction in Training Time
| 1 | 2 | 4 | 6 | 8 | 10
Series 1 | 0 | 26.502 | 39.967 | 44.5262 | 46.592 | 48.991
Cooperative MARL
Competitive MARL
Notation:
= Parallel agents/environments
= Number of agents per family

## Slide 30: Conclusion
Scalable and Parallelizable Multi-Agent Reinforcement Learning for AVs

## Slide 31
Summary
Digital twin creation
  Geometric measurements & modeling
  Static measurements & calibration
  Simulation models (dynamics + graphics)
  Physics-based sensor simulation
Scalable multi-agent reinforcement learning
  Vanilla RL (1 agent problem in dynamic environment)
  Vanilla RL (4 agent cooperative problem)
  Demonstration guided RL (2 agent competitive problem)
Modular and parallelizable simulation
  Environment parallelization
  Agent parallelization
  Computational analysis

## Slide 32
Future Plans
Analyze RL training across different types of computing platforms
  Laptops, desktops, workstations, Palmetto HPC (different configs.)
Integrated digital twin framework for sim2real transfer of MARL
  1 physical vehicle
  Virtual peers/competitors in loop with the physical vehicle
Physics informed RL
  State transition models, physics-informed rewards, safety guarentees, etc.
Extend this approach to different vehicles and architectures
Husky (On/Off-Road Skid-Steer Robot)
Hunter SE (On/Off-Road Ackermann Steered Vehicle)
Nigel (Native Vehicle)
F1TENTH (1/10th Scale Racecar)
RZR (Recreational Off-Highway Vehicle)
OpenCAV (On-Road Commercial Vehicle)
SMALL-SCALE
MID-SCALE
FULL-SCALE

## Slide 33: Thank You!
…open to questions and suggestions

## Slide 34
T. Samak, C. Samak, S. Kandhasamy, V. Krovi, and M. Xie, “AutoDRIVE: A Comprehensive, Flexible and Integrated Digital Twin Ecosystem for Autonomous Driving Research & Education,” Robotics, vol. 12, no. 3, p. 77, May 2023, doi: 10.3390/robotics12030077
W. Ding, C. Xu, M. Arief, H. Lin, B. Li and D. Zhao, “A Survey on Safety-Critical Driving Scenario Generation—A Methodological Perspective,” in IEEE Transactions on Intelligent Transportation Systems, vol. 24, no. 7, pp. 6971-6988, July 2023, doi: 10.1109/TITS.2023.3259322
S. H. Semnani, H. Liu, M. Everett, A. de Ruiter, and J. P. How, “Multiagent Motion Planning for Dense and Dynamic Environments via Deep Reinforcement Learning,” 2020.
P. Long, T. Fan, X. Liao, W. Liu, H. Zhang, and J. Pan, “Towards Optimally Decentralized Multi-Robot Collision Avoidance via Deep Reinforcement Learning,” 2018
S. Aradi, “Survey of Deep Reinforcement Learning for Motion Planning of Autonomous Vehicles,” 2020.
D. Wang, H. Deng, and Z. Pan, “MRCDRL: Multi-Robot Coordination with Deep Reinforcement Learning,” Neurocomputing, 2020.
X. Zhou, P. Wu, H. Zhang, W. Guo, and Y. Liu, “Learn to navigate: cooperative path planning for unmanned surface vehicles using deep reinforcement learning,” IEEE Access, vol. 7, pp. 165 262–165 278, 2019.
References

## Slide 35
K. Sivanathan, B. K. Vinayagam, T. Samak, and C. Samak, “Decentralized Motion Planning for Multi-Robot Navigation using Deep Reinforcement Learning,” in 2020 3rd International Conference on Intelligent Sustainable Systems (ICISS), 2020, pp. 709–716, doi: 10.1109/ICISS49785.2020.9316033
F. Fuchs, Y. Song, E. Kaufmann, D. Scaramuzza, and P. Durr, “Super-Human Performance in Gran Turismo Sport Using Deep Reinforcement Learning,” IEEE Robotics and Automation Letters, vol. 6, no. 3, pp. 4257–4264, 2021.
Y. Song, H. Lin, E. Kaufmann, P. Durr, and D. Scaramuzza, “Autonomous Overtaking in Gran Turismo Sport Using Curriculum Reinforcement Learning,” 2021.
C. V. Samak, T. V. Samak, and S. Kandhasamy, “Autonomous Racing using a Hybrid Imitation-Reinforcement Learning Architecture,” 2021. [Online]. Available: https://arxiv.org/abs/2110.05437
J. Betz, H. Zheng, A. Liniger, U. Rosolia, P. Karle, M. Behl, V. Krovi, and R. Mangharam, “Autonomous Vehicles on the Edge: A Survey on Autonomous Vehicle Racing,” IEEE Open Journal of Intelligent Transportation Systems, vol. 3, pp. 458–488, 2022.
References